## Slide 1
April 25, 2013
Edward Venator
A Low-Cost Mobile Manipulator for Industrial and Research Applications
Notes: Thank you Professor Lee.
As Professor Lee said, I’m Ed Venator, and today I’ll be presenting my thesis, which is on the creation of a low-cost mobile manipulator for industrial and research applications.

## Slide 2
Introduction
Notes: I’ll start with a brief introduction to the project
What I did – developed a mobile industrial manipulator
Why I did it (goals)
  To be used for industrial kitting research
  To be used for human-robot interaction research
  Low cost
  Robust
What I used – commercial off the shelf hardware, open source software
  Talk about this more later

## Slide 3
AGV photo courtesy Wikipedia (http://en.wikipedia.org/wiki/File:Agv.forktruck2.jpg)
IRB-120/IRC5 photo courtesy ABB (http://www.abb.com/product/seitp327/BE2EEF38406EACA4C125762000319182.aspx)
PR2 photo courtesy Willow Garage (http://www.willowgarage.com/blog/2011/08/10/announcing-pr2se)
DARPA ARM Robot photo courtesy Hizook.com (http://www.hizook.com/blog/2012/04/03/new-darpa-grand-challenge-humanoid-robots-preliminary-unofficial-details)
IMP photo from Hardware and Software Architecture of a Bimanual Mobile Manipulator for Industrial Application (Proceedings of the 2011 IEEE International Conference on Robotics and Biomimetics)
Background
Notes: Before I talk more about what I did, some background on industrial and research robotics.
Industry – Robots divided between mobile robots and robotic arms
Mobile robots like Automated Guided Vehicles (AVGs) and Kiva robot
  AGVs are things like forklifts that move pallets along predefined paths
  Kiva Systems mobile robot has more freedom than an AGV, but only moves shelves and pallets, relies on human pickers
Robotic arms
  Dexterous
  Stationary
  Usually follow preprogrammed paths
Lack of industrial mobile manipulators
Lack of robots taking advantage of dynamic planning
Academic
“Research grade” hardware is not robust
Mention DARPA ARM, Verona and IMP
(IMP is a 2011 project of the Intelligent Systems and Production Engineering Research Center for Information in Karlsruhe, Germany)
Hardware is very expensive
  PR2 ($285k)
  Barrett arm $30k each + end effector
Research/academic vs Industrial
  Research hardware is Capable, but industrial hardware is cheap
  Industrial hardware also more robust
  Research software is Smart, but industrial software is reliable and safe
  Research platforms are custom-made and Experimental, and industrial platforms are standardized (exception is PR2)
Seeing a new interest in smarter, lighter industrial manipulators
  Baxter (Rethink Robotics)
  ABB Frieda (ABB)
  UR-5 and UR-10 (Universal Robots)

## Slide 4
Goals
Mobile manipulation
Robustness
Extensibility
Low Cost
  Mass produced manipulator
  Mass produced mobile base
  Consumer grade sensor
Notes: All of these things motivate this project.
The Goals of the project are:
Mobile manipulation
Mobile manipulators nearly non-existent in industry
Mobile manipulators can replace human workers for many tasks
Mobile manipulator can be used to retrieve parts from inventory
Mobile manipulator can be used for reconfigurable manufacturing
Robustness
Research grade hardware typically has a high failure rate
On the other hand, industrial hardware is typically tested and hardened against failure
Industrial hardware has built-in safety (one example is motion supervision)
Using industrial hardware in a research platform results in a more robust, safer research robot
Extensibility – This is a platform for future research
The robot has basic capabilities, including navigation and simple arm motion
The software system must be modular to allow future researchers to experiment with new algorithms
The sensors should be usable by future researchers for human-sensing
Low cost – compared to research grade
PR2 Costs $285k
DARPA ARM Costs >$66k
Leverage commercially-available hardware to reduce cost

## Slide 5
ABBY – Physical Design
Notes: Physical Design
The robot I created to address these goals is called ABBY
ABBY is a mobile industrial manipulator
Invacare Electric wheelchair base
  130 kilogram Payload
  Top speed of 2.9 meter/second
  Power source – 24 volt lead acid battery
IRB-120 Robot Arm
  3 kilogram Payload
  0.6 meter reach
  0.1 millimeter Precision
  Powered from AC Inverter from the drive base batteries
Plastic carrier bin
  Holds parts that have been picked up by the arm

## Slide 6
Sensing and Computing
Ethernet
USB
Other
Notes: Sensing and computing
PC
  4 core Intel processor, 8GB RAM
  Ubuntu desktop Operating System
  Robot Operating System (you’ll talk more about this on the next slide)
  Runs all higher level planning
IRC5
  Required to control IRB-120 arm
  Realtime Operating System that runs RAPID code
  RAPID is proprietary and kind of clunky
  Runs minimal code to control the arm (talk more about this later)
cRIO (it really doesn’t deserve much time)
  Used to control drive base and perform odometry using drive base encoders
Kinect
  Low cost Red-Green-Blue-Depth (3D) camera mounted high on the robot mast looking down into the manipulator work envelope
  Designed as a video game controller
  Used as a lower-accuracy replacement for binocular vision systems and tilting laser scanners
  Used for obstacle detection and object detection for the manipulator
LIDAR
  SICK LMS-291 mounted to the front of the robot
  One of the more expensive components of the robot
  Used for obstacle detection and absolute localization by the mobile base

## Slide 7
Robot Operating System (ROS)
Notes: Feature – ROS
ROS is a modular system for managing multiprocess robotic software
  ROS nodes can be easily swapped out to try out different algorithms
  ROS handles interprocess communication
  This is a network graph of the software running on ABBY
    Messages can be sent between nodes (shown in black)
    Nodes can provide services to other nodes (shown in blue)
    Nodes can provide action servers, which are like services, but use a state machine architecture to provide feedback on the process they perform (shown in red)
ROS has existing capabilities, created by other researchers, which I leveraged in this project
  Robot state modeling
  Sensor drivers for Kinect and LIDAR
  Localization (AMCL)
  Mobile base navigation
  Arm trajectory planning
  Basic object recognition
  Process management, GUI tools

## Slide 8
ROS Industrial
Project of Southwest Research Institute
Allows ROS to be used with industrial robots
Standardized interface
This project jumpstarted development of the ROS Industrial ABB driver
Notes: Feature – ROS Industrial
What is ROS Industrial?
  Project of Southwest Research Institute
  Does most of arm planning on PC in ROS
  Minimal software on the IRC5 controller (trajectory server, state server, motion process)
How does it work?
  Uses the ROS standard arm navigation stack for path planning
  ROS PC sends a trajectory download to the IRC5
  Trajectory defined as sequence of points, each point defined by joint angles
  IRC5 receives trajectory, executes it by visiting each point in sequence
  No torque control (limitation of IRC5 and of ROS Industrial)
  No velocity control (limitation of ROS Industrial)
  IRC5 reports joint states to ROS PC over the network
Why did I use ROS Industrial?
  Standard platform – many industrial robotic arms supported
  Gaining traction amongst researchers
  Speeded development
How did I contribute to ROS Industrial?
  Wrote original ABB arm driver – ROS node and RAPID code
  This code is the basis for the ROS Industrial ABB code, which has been improved and released

## Slide 9
Cost
Item | Cost
Wheelchair Base + batteries | $3400
Chassis Frame Materials | $1000
LIDAR | $6000
IRB-120/IRC5 | $23000
cRIO 9074 | $4150
PC | $547
Kinect | $150
Grayhill Encoder (4) | $320
Emergency Stop System | $160
AC Inverter | $322
Sabertooth 2x50 | $250
Compressor | $250
Network Equipment | $40
Miscellaneous Electrical Components | $286
Total | $39875
Notes: Feature – Cost
Total cost is less than $40,000
Big-ticket items
  IRB-120/IRC5 (still cheaper than a research manipulator)
  SICK LIDAR (free for this project, might be replaceable with a cheaper LIDAR)
  cRIO (free for this project, might be replaceable with a cheaper controller)
Compare to
  PR2 (over $200,000)
  DARPA ARM (not mobile, over $60,0000)

## Slide 10
Navigation
Notes: Capability – Navigation
This robot can perform all of the tasks necessary for autonomous mobile navigation
Localization
  Relative localization using odometry at 50Hz
  Absolute localization using Adapative Monte Carlo Localization at up to 5Hz
  AMCL matches LIDAR scan data to an a priori map to get an absolute position estimate
Global planning
  Plans a path through an occupancy grid generated from LIDAR scan data
  Path generation using the ROS node NavFN, which plans using Djikstra’s algorithm
  The paths are not guaranteed to be valid for non-circular robots
Trajectory generation
  Velocity commands generated at 12 Hz using trajectory rollout
  Trajectory rollout forward-simulates velocity commands and selects one according to a cost function that favors motion toward the path, motion toward the goal, and motion away from obstacles
The path planning system was tested to determine how well it can navigate to predefined waypoints
  The map above shows the task
  Navigation was tested by driving from one of two start positions (green) to a table several meters away (blue) and then to a final position
  This task is challenging for the navigation system because it must approach very close to the table, which it perceives as an obstacle
  The final position is also relatively close to obstacles

## Slide 11
Trial | Start Position | Drive To Table | Drive to Final Position
1 | Left | Successful | Several spins at goal position before success
2 | Left | Successful | Several spins at goal position before success
3 | Left | Successful | Successful
4 | Left | Successful | Successful
5 | Left | Successful | Successful
6 | Left | Successful | Successful
7 | Left | Successful | Successful
8 | Left | Successful | Several spins at goal position before success
9 | Right | Successful | Successful
10 | Right | Successful | Successful
11 | Right | Successful | Successful
12 | Right | Successful | Successful
13 | Right | Successful | Successful
14 | Right | Successful | Successful
15 | Right | Successful | Successful
16 | Right | Successful | Arrives at goal position, then spins several times and the gripper brushes an obstacle
Chart: 
| Qualified Success | Failure | Success
Navigation Results | 3 | 1 | 12
Notes: Results – Navigation
Here are the results of the navigation test
The majority of trials were successful, with 75% performing the task perfectly
Some trials were classified as a qualified success – The robot reached the goal location, but spun in place one or more times before settling at the goal heading
In one trial, the robot never recovered from the spinning behavior, and the robot was stopped when it brushed an obstacle
The possible causes of the spinning:
  Poor low-level control in the drive base (because of the motor speed controllers used and the control architecture previously developed for these wheelchair robots)
  Overloading the PC’s CPU, resulting in low update rates from the local planner. Update rates as low as 3Hz were observed.

## Slide 12
Odometry circle data table
Odometry circle scatter plot
Trial | X | Y | Displacement | Position Error
1 | 9.535 | -2.908 | 9.969 | 2.945
2 | 10.042 | -0.760 | 10.071 | 0.761
3 | 10.373 | -0.032 | 10.373 | 0.374
4 | 9.996 | -0.454 | 10.005 | 0.454
5 | 9.881 | -0.663 | 9.903 | 0.674
6 | 10.019 | -0.610 | 10.036 | 0.610
RMS | 9.977 | 1.294 | 10.060 | 1.318
STD | 0.271 | 1.016 | 0.164 | 0.978
Trial | x | y | Oz | Ow | Displacement | Heading (deg)
1 | 0.730 | 0.432 | 0.507 | 0.862 | 0.849 | 29.124
2 | 0.802 | 0.45 | 0.528 | 0.849 | 0.920 | 26.202
3 | 0.941 | 0.596 | 0.613 | 0.790 | 1.114 | 14.370
4 | 0.751 | 0.621 | 0.558 | 0.830 | 0.974 | 22.150
5 | 0.778 | 0.330 | 0.459 | 0.889 | 0.845 | 35.404
6 | 0.892 | 0.434 | 0.502 | 0.865 | 0.992 | 29.677
RMS | 0.819 | 0.488 | 0.530 | 0.848 | 0.954 | 26.975
STD | 0.0833 | 0.111 | 0.053 | 0.034 | 0.101 | 7.235
Notes: Results – odometry
I characterized the odometry system to determine whether an absolute localization system would be necessary for this robot.
Two tests were performed
In the Straight line test, the robot was driven for 10 meters in a straight line
In the Circle test, the robot was driven through five laps of a 1 meter radius circle
Results show that odometry is not sufficient for localization
I’ve plotted the path the robot traveled in green
The red mark is the actual position of the robot at the end of the test
The blue marks are the results of the trials, which are also shown in the tables below
These results show that the robot needs absolute localization to supplement odometry
I used Adaptive Monte Carlo Localization (AMCL) for absolute localization

## Slide 13
Manipulation
Notes: Capability – Manipulation
Explain portions of manipulation task
Tabletop Object recognition
Object location (bounding boxes)
Rudimentary grasp planning
Arm motion stow->pregrasp->grasp
Gripper closes
Arm motion grasp->retreat
Arm motion retreat->store
Gripper opens
Arm motion store->stow

## Slide 14
Trial | Objects Recognized | Pick Result | Drop Result
1 | 3 | Success | Success
2 | 3 | Success | Success
3 | 3 | Success | Success
4 | 2 | Success ( 3rd attempt) | Success
5 | 2 | Missed (gripper nudges table) | Success (with no object)
6 | 2 | Success ( 2nd attempt) | Success
7 | 3 | Success | Success
8 | 4 | Success ( 2nd attempt) | Success
9 | 2 | Success, insecure grip ( 3rd attempt) | Success (object fell)
10 | 3 | Missed | Success (with no object)
11 | 2 | Missed | Success (with no object)
12 | 2 | Success | Success
13 | 2 | Missed (gripper nudges table) | Success (with no object)
14 | 2 | Success (2nd attempt) | Success
15 | 1 | Cannot find a path to the object | N/A
16 | 2 | Gripper hits table | N/A
17 | 2 | Gripper hits table | N/A
18 | 2 | Success | Success
19 | 3 | Success | Success
20 | 2 | Gripper hits table | N/A
21 | 1 | Success, insecure grip ( 3rd attempt) | Success (object fell)
22 | 2 | Success | Success (takes over 60 s)
23 | 2 | Gripper hits table | N/A
24 | 3 | Success | Success
25 | 2 | Missed | Success (with no object)
Chart: 
| Missed Pick | Collision with Table | Success | No Path to Object
Manipulation Results | 3 | 6 | 15 | 1
Notes: Results
The majority of the trials (60%) are successful
Failures primarily due to the gripper colliding with the table
  Cause unknown
  Arm planner should plan collision-free trajectories
  Collision-checking appears to be neglecting the gripper
  This is an area of future work
Some failures (12%) are due to the robot missing the object it’s attempting to pick up
  Objects are 5 cm diameter; gripper is 5.3 cm opening
In one trial, the robot could not find a path to move the gripper to the object
  In this trial, the arm occluded the Kinect’s view of 2 out of 3 objects on the table
  Object grasping code is rudimentary, meant as a proof-of-concept, and only attempts one grasp angle

## Slide 15
Simulated Kitting Task
  Beginning at one of two starting locations, drive to a predetermined location near a table a few meters away.
  Locate at least one of three small manipulable objects on the table using the Kinect.
  Lift one of the target objects from the table.
  Place the target object in the onboard carrier bin.
  Drive to the final destination.
Notes: Capability – Simulated Kitting Task
This test is meant to simulate the task of getting at object from inventory and bringing it to an assembly station
The task is a combination of navigation and manipulation tasks
  Beginning at one of two starting locations, drive to a predetermined location near a table a few meters away.
  Locate at least one of three small manipulable objects on the table using the Kinect.
  Lift one of the target objects from the table.
  Place the target object in the onboard carrier bin.
  Drive to the final destination.
The table represents a shelf
The cylindrical objects represent parts for an assembly
In a real situation, steps 1-4 are repeated until all objects in the kit are picked up

## Slide 16
Trial | Start Position | Objects Recognized | Notes
1 | Left | 2 | Robot spins before settling into final position
2 | Left | 2 | Gripper brushes table and knocks over 1 object; robot spins before settling into final position
3 | Left | N/A | Robot approaches table, but get stuck in spin
4 | Left | 1 | Object recognition/pickup succeeds on fourth attempt
5 | Right | 1 | Low batteries prevent robot from aligning in final position
6 | Right | 2 | 
7 | Right | 1 | Low batteries prevent robot from aligning in final position
8 | Right | 3 | Robot spins before settling into final position
Chart: Simulated Kitting Results
| Failure | Success
Simualted Kitting Results | 1 | 7
Notes: Results
The majority of these trials were successful
The spinning behavior from the navigation tests still is still evident
In fact, the single failure observed here is a result of the spinning behavior (only time this was observed at the table)
The spinning behavior at the table was rare, which is illustrated in the manipulation task, which begins with an approach to the table

## Slide 17
Notes: Results – Mobile manipulation
Manipulation is at double speed
Navigation shows two trials
First trial shows the spinning behavior in the qualified successes from the results
Second trial is a perfect navigation trial
This is the second trial again, but showing the robot state in the ROS rviz tool
Video 2 -3 minutes

## Slide 18
Questions
Thanks To
ABB (for loan of the IRB-120 and IRC5)
Dr. Wyatt Newman (former advisor on the project)
Dr. Gregory Lee (project advisor)
Dr. Chris Roberts, Eric Perko, and Chad Rockey