## Slide 1
April 25, 2013
Edward Venator
A Low-Cost Mobile Manipulator for Industrial and Research Applications

## Slide 2
Introduction
Not sure what to put here
Need a pic here
Notes: Introduction
What I did – developed a mobile industrial manipulator
What I used – commercial off the shelf hardware, open source software
Why I did it (goals)
  To be used for industrial kitting research
  To be used for human-robot interaction research
  Low cost
  Robust
How long I worked on it – 15 months

## Slide 3
AGV photo courtesy Wikipedia (http://en.wikipedia.org/wiki/File:Agv.forktruck2.jpg)
IRB-120/IRC5 photo courtesy ABB (http://www.abb.com/product/seitp327/BE2EEF38406EACA4C125762000319182.aspx)
PR2 photo courtesy Willow Garage (http://www.willowgarage.com/blog/2011/08/10/announcing-pr2se)
DARPA ARM Robot photo courtesy Hizook.com (http://www.hizook.com/blog/2012/04/03/new-darpa-grand-challenge-humanoid-robots-preliminary-unofficial-details)
IMP photo from Hardware and Software Architecture of a Bimanual Mobile Manipulator for Industrial Application (Proceedings of the 2011 IEEE International Conference on Robotics and Biomimetics)
Notes: Background
This is a little busy. Clean it up (maybe 2 slides?)
Industry
AGVs vs manipulators
Lack of industrial mobile manipulators
Academic
“Research grade” hardware is not robust
Hardware is very expensive
  PR2 ($285k)
  Barrett arm $30k each + end effector
Mention DARPA ARM, Verona and IMP
Research/academic vs Industrial
  Capable vs cheap
  Smart vs reliable
  Experimental vs standardized (exception is PR2)
Seeing a new interest in smarter, lighter industrial manipulators
  Baxter
  ABB Frieda
  Universal robot

## Slide 4
Goals
Mobile manipulation
Robustness
Extensibility
Low Cost
  Mass produced manipulator
  Mass produced mobile base
  Consumer grade sensor
Need a pic here…
Notes: Mobile manipulation
Mobile manipulators nearly non-existent in industry
Mobile manipulator replaces a human worker for many tasks
Mobile manipulator can be used to retrieve parts from inventory
Mobile manipulator can be used for reconfigurable manufacturing
Robust
Research grade hardware typically has high failure rate
Industrial hardware typically tested and hardened against failure
Industrial hardware has safety (motion supervision)
Extensibility – This is a platform for future research
Robot has basic capabilities
Software system must be modular to allow future researchers to experiment with new algorithms
Sensors should be usable by future researchers for human-sensing
Low cost – compared to research grade
PR2 Costs $285k
DARPA ARM Costs >$66k
Leverage commercially-available hardware to reduce cost

## Slide 5
ABBY – Physical Design
Notes: Physical Design
Invacare Electric wheelchair base
  Payload –
  Speed –
  Power source – battery capacity
IRB-120 Robot Arm

## Slide 6
Sensing and Computing
Notes: Sensing and computing
PC
  4 core Intel processor, 8GB RAM
  Ubuntu desktop OS
  Robot Operating System (you’ll talk more about this on the next slide)
  Runs all higher level planning
IRC5
  Required to control IRB-120 arm
  Realtime OS that runs RAPID code
  RAPID is proprietary and kind of clunky
  Runs minimal code to control the arm (you’ll talk more about this later)
cRIO (it really doesn’t deserve much time)
  Used to control drive base and perform odometry using drive base encoders
Kinect
  Low cost RGBD camera mounted high on the robot mast looking down into the manipulator work envelope
  Designed as a video game controller
  Used as a lower-accuracy replacement for binocular vision systems and tilting laser scanners
  Used for obstacle detection and object detection for the manipulator
LIDAR
  SICK LMS-291 mounted to the front of the robot
  One of the more expensive components of the robot
  Used for obstacle detection and absolute localization by the mobile base

## Slide 7
Robot Operating System (ROS)
ROS Graph
Rviz screen? Probably not
Notes: Feature – ROS
ROS is modular and awesome
ROS has existing capabilities
  Robot state modeling
  Sensor drivers for Kinect and LIDAR
  Localization (AMCL)
  Mobile base navigation
  Arm trajectory planning
  Process management, GUI tools

## Slide 8
ROS Industrial
Notes: Feature – ROS Industrial
Picture of arm in Rviz? ROS-I logo? ROS-I block diagram? Arm motion video?
What is ROS-I?
  Project of SWRI
  Does most of arm planning on PC in ROS
  Minimal software on the IRC5 controller (trajectory server, state server, motion process)
Why did I use ROS-I?
  Standard platform – many arms supported
  Gaining traction amongst researchers
  Speeded development
How did I contribute to ROS-I?
  Wrote original ABB arm driver – ROS node and RAPID code
  This code is the basis for the ROS-I ABB code, which has been improved and released
How does it work?
  Uses the ROS standard arm navigation stack for path planning
  ROS PC sends a trajectory download to the IRC5
  Trajectory defined as sequence of points, each point defined by joint angles
  IRC5 receives trajectory, executes it by visiting each point in sequence
  No torque control (limitation of IRC5 and of ROS-I)
  No velocity control (limitation of ROS-I)
  IRC5 reports joint states to ROS PC over the network

## Slide 9
Navigation
Replace with a pic with table and start locations
Notes: Capability – Navigation
What this robot can do
Localization
Global planning
Trajectory generation
How done
*

## Slide 10
Odometry circle data table
Odometry circle scatter plot
Trial | X | Y | Displacement | Position Error
1 | 9.535 | -2.908 | 9.969 | 2.945
2 | 10.042 | -0.760 | 10.071 | 0.761
3 | 10.373 | -0.032 | 10.373 | 0.374
4 | 9.996 | -0.454 | 10.005 | 0.454
5 | 9.881 | -0.663 | 9.903 | 0.674
6 | 10.019 | -0.610 | 10.036 | 0.610
RMS | 9.977 | 1.294 | 10.060 | 1.318
STD | 0.271 | 1.016 | 0.164 | 0.978
Trial | x | y | Oz | Ow | Displacement | Heading (deg)
1 | 0.730 | 0.432 | 0.507 | 0.862 | 0.849 | 29.124
2 | 0.802 | 0.45 | 0.528 | 0.849 | 0.920 | 26.202
3 | 0.941 | 0.596 | 0.613 | 0.790 | 1.114 | 14.370
4 | 0.751 | 0.621 | 0.558 | 0.830 | 0.974 | 22.150
5 | 0.778 | 0.330 | 0.459 | 0.889 | 0.845 | 35.404
6 | 0.892 | 0.434 | 0.502 | 0.865 | 0.992 | 29.677
RMS | 0.819 | 0.488 | 0.530 | 0.848 | 0.954 | 26.975
STD | 0.0833 | 0.111 | 0.053 | 0.034 | 0.101 | 7.235
Notes: Results – odometry
Maybe rerun these tests w/ AMCL for comparison
Two tests performed
Straight line test – robot is driven for 10 meters in a straight line
Circle test – robot is driven through five laps of a 1 meter radius circle
Results show that odometry is not sufficient for localization
Green is path traveled, red is actual position, and blue are trial results
Absolute localization needs to supplement odometry
AMCL used for absolute localization

## Slide 11
Trial | Start Position | Drive To Table | Drive to Final Position
1 | Left | Successful | Several spins at goal position before success
2 | Left | Successful | Several spins at goal position before success
3 | Left | Successful | Successful
4 | Left | Successful | Successful
5 | Left | Successful | Successful
6 | Left | Successful | Successful
7 | Left | Successful | Successful
8 | Left | Successful | Several spins at goal position before success
9 | Right | Successful | Successful
10 | Right | Successful | Successful
11 | Right | Successful | Successful
12 | Right | Successful | Successful
13 | Right | Successful | Successful
14 | Right | Successful | Successful
15 | Right | Successful | Successful
16 | Right | Successful | Arrives at goal position, then spins several times and the gripper brushes an obstacle
Chart: 
| Qualified Success | Failure | Success
Navigation Results | 3 | 1 | 12
Notes: Results – Navigation

## Slide 12
Short manipulation video
Manipulation
Notes: Capability – Manipulation
Show short video
Explain portions of manipulation task
Tabletop Object recognition
Object location (bounding boxes)
Rudimentary grasp planning
Arm motion stow->pregrasp->grasp
Gripper closes
Arm motion grasp->retreat
Arm motion retreat->store
Gripper opens
Arm motion store->stow

## Slide 13
Trial | Objects Recognized | Pick Result | Drop Result
1 | 3 | Success | Success
2 | 3 | Success | Success
3 | 3 | Success | Success
4 | 2 | Success ( 3rd attempt) | Success
5 | 2 | Missed (gripper nudges table) | Success (with no object)
6 | 2 | Success ( 2nd attempt) | Success
7 | 3 | Success | Success
8 | 4 | Success ( 2nd attempt) | Success
9 | 2 | Success, insecure grip ( 3rd attempt) | Success (object fell)
10 | 3 | Missed | Success (with no object)
11 | 2 | Missed | Success (with no object)
12 | 2 | Success | Success
13 | 2 | Missed (gripper nudges table) | Success (with no object)
14 | 2 | Success (2nd attempt) | Success
15 | 1 | Cannot find a path to the object | N/A
16 | 2 | Gripper hits table | N/A
17 | 2 | Gripper hits table | N/A
18 | 2 | Success | Success
19 | 3 | Success | Success
20 | 2 | Gripper hits table | N/A
21 | 1 | Success, insecure grip ( 3rd attempt) | Success (object fell)
22 | 2 | Success | Success (takes over 60 s)
23 | 2 | Gripper hits table | N/A
24 | 3 | Success | Success
25 | 2 | Missed | Success (with no object)
Chart: 
| Missed Pick | Collision with Table | Success | No Path to Object
Manipulation Results | 3 | 6 | 15 | 1
Notes: Results
Data - manipulation

## Slide 14
Simulated Kitting Task
  Beginning at one of two starting locations, drive to a predetermined location near a table a few meters away.
  Locate at least one of three small manipulable objects on the table using the Kinect.
  Lift one of the target objects from the table.
  Place the target object in the onboard carrier bin.
  Drive to the final destination.
Notes: Capability – Simulated Kitting Task

## Slide 15
Trial | Start Position | Objects Recognized | Notes
1 | Left | 2 | Robot spins before settling into final position
2 | Left | 2 | Gripper brushes table and knocks over 1 object; robot spins before settling into final position
3 | Left | N/A | Robot approaches table, but get stuck in spin
4 | Left | 1 | Object recognition/pickup succeeds on fourth attempt
5 | Right | 1 | Low batteries prevent robot from aligning in final position
6 | Right | 2 | 
7 | Right | 1 | Low batteries prevent robot from aligning in final position
8 | Right | 3 | Robot spins before settling into final position
Chart: Simulated Kitting Results
| Failure | Success
Simualted Kitting Results | 1 | 7
Notes: Results
Data – Combined Task

## Slide 16
Highlight reel video
Notes: Results – Mobile manipulation
Video 2 -3 minutes

## Slide 17
Questions
Thanks To
ABB (for loan of the IRB-120 and IRC5)
Dr. Wyatt Newman (former advisor on the project)
Dr. Gregory Lee (project advisor)
Dr. Chris Roberts, Eric Perko, and Chad Rockey